## Slide 1
OPERATIONS RESEARCH · METAHEURISTIC OPTIMIZATION
Active Space Debris Removal
Mission Planning Optimized with Simulated Annealing
Sequencing debris removal to minimize fuel, time, and cost — while maximizing collision-risk reduction
Fuel (ΔV)
Mission Time
Cost
Risk Removed

## Slide 2
The Problem
Orbit is getting crowded
Active Space Debris Removal (ASDR) plans a single-spacecraft mission that visits a set of debris objects in orbit, choosing the sequence and transfers that clear the most collision risk within a limited fuel and time budget.
Which order to visit debris in
A routing decision — every sequence changes total fuel and time.
Which debris to prioritize
Riskier, heavier objects matter more to remove first.
How to stay within mission limits
Fuel and duration constraints must never be violated.
One spacecraft.
Many debris. One shot at an efficient route.
Every extra debris object multiplies the number of possible mission plans — this is what makes ASDR computationally hard.
ASDR · Simulated Annealing Optimization
02

## Slide 3
Complexity
Why ASDR is NP-hard
ASDR bundles four hard decisions at once: which debris to select, what order to visit them in, how much fuel to allocate, and how to satisfy mission constraints. With N debris objects, the number of possible visit sequences is N! — exhaustive search becomes impossible almost immediately.
ASDR generalizes several classical NP-hard problems:
Traveling Salesman
Vehicle Routing
Orienteering
Knapsack
Scheduling
Sequences grow factorially
N = 5
120
N = 8
40,320
N = 10
3,628,800
N = 20
2.43 × 10¹⁸
Bar length shown on a log scale — the actual gap between N=10 and N=20 is many trillion-fold.
Number of Debris Objects (N) → Possible Visit Sequences
ASDR · Simulated Annealing Optimization
03

## Slide 4
Formulation
Decision Variables & Objective
The optimizer determines
x₁
Sequence of debris removal
x₂
Next debris object to visit
x₃
Orbital transfer between debris
x₄
Total fuel (ΔV) allocation
x₅
Mission schedule
Weighted Objective (minimize)
J = w1(ΔV) + w2(Time) + w3(Cost) − w4(Risk Removed)
ΔV — total fuel consumption
Time — total transfer duration
Cost — mission time × hourly rate
Risk Removed — sum of debris risk scores
A large penalty is added whenever the fuel constraint is violated.
ASDR · Simulated Annealing Optimization
04

## Slide 5
Constraints
What every valid mission must satisfy
Fuel Capacity Limit
Cumulative ΔV across the whole route must not exceed the mission fuel budget.
Mission Duration
Total transfer time is bounded by the planned mission window.
One Visit per Object
Each debris object is removed exactly once — no repeats, none skipped twice.
Valid Orbital Transfers
Only physically reachable transfers between orbital states are allowed.
Single Spacecraft
One vehicle executes the entire removal sequence, in order.
No Duplicate Removal
A debris object cannot be counted or removed more than once.
Penalty functions discourage the optimizer from wandering into infeasible solutions.
ASDR · Simulated Annealing Optimization
05

## Slide 6
Cost Model
Estimating fuel & time between debris
Transfer ΔV
ΔVij = 0.4 · |Alti − Altj| + 25 · |Inci − Incj|
0.4 km/km weight on altitude change, plus a 25 m/s per degree weight on inclination change — inclination shifts dominate real ΔV budgets, and the model reflects that.
Fuel limit: Σ ΔV ≤ 450
Mission Time
Timeij = |Alti−Altj| / 25 + 4·|Inci−Incj|
≈25 km of altitude change costs about one hour; every degree of inclination change adds four hours — plane changes are the slow, expensive part of any transfer.
Operational Cost = Time × $5,000/hr
ASDR · Simulated Annealing Optimization
06

## Slide 7
Optimization Core
Penalty & Acceptance Rules
Fuel Constraint
Σ ΔV ≤ Fuel_limit
Any route exceeding this is infeasible.
Penalty Function
Penalty = 100,000 if infeasible
A large fixed penalty is added to J whenever the fuel limit is broken — steering the search back toward feasible routes without forbidding exploration.
Metropolis Acceptance
P = e^(−Δ / T)
Worse solutions (Δ > 0) are still accepted with probability P — this is how Simulated Annealing escapes local optima.
ASDR · Simulated Annealing Optimization
07

## Slide 8
Algorithm
How Simulated Annealing searches for a plan
1
Random Initial Sequence
Start from a randomly ordered mission plan.
›
2
Generate a Neighbor
Swap, reverse, or insert debris within the sequence.
›
3
Evaluate the Objective
Score the new sequence using J (ΔV, time, cost, risk).
›
4
Metropolis Acceptance
Accept improvements always; accept worse moves with probability e^(−Δ/T).
›
5
Cool the Temperature
Reduce T geometrically: T_new = 0.995 × T_old.
›
6
Track the Best Solution
Repeat until T falls below the minimum threshold.
1000
Initial Temperature
0.995
Cooling Rate (α)
0.01
Minimum Temperature
ASDR · Simulated Annealing Optimization
08

## Slide 9
Case Study
Example debris field — 8 objects
Debris | Altitude (km) | Inclination (°) | Mass (kg) | Risk
D1 | 700 | 98.2 | 1200 | 0.82
D2 | 720 | 97.8 | 900 | 0.65
D3 | 680 | 98.6 | 1400 | 0.91
D4 | 750 | 99.1 | 1600 | 0.93
D5 | 690 | 97.9 | 850 | 0.72
D6 | 710 | 98.4 | 1000 | 0.79
D7 | 740 | 99.4 | 1500 | 0.95
D8 | 730 | 98.7 | 1300 | 0.87
Highest-risk objects (highlighted) drive most of the removed-risk value in the objective function.
Risk Score by Object
Chart: 
| D1 | D2 | D3 | D4 | D5 | D6 | D7 | D8
Risk | 0.82 | 0.65 | 0.91 | 0.93 | 0.72 | 0.79 | 0.95 | 0.87
ASDR · Simulated Annealing Optimization
09

## Slide 10
Result
Optimized removal sequence
D5
→
D2
→
D1
→
D6
→
D8
→
D7
→
D4
→
D3
Best objective score: J = 24,396.87
381.40 m/s
Total ΔV
52.80 hr
Mission Time
$264,000
Operational Cost
6.64
Risk Removed
Fuel Constraint Satisfied
ASDR · Simulated Annealing Optimization
10

## Slide 11
Convergence
How the objective improves over iterations
The objective drops sharply while temperature is high — the search explores broadly and accepts many worse moves — then settles into a stable near-optimal value as cooling progresses.
Chart: Iteration
| 0 | 50 | 100 | 150 | 200 | 300 | 400 | 500 | 650 | 800 | 1000
Objective Value J | 26800 | 25600 | 24900 | 24550 | 24430 | 24410 | 24400 | 24398 | 24397 | 24396.9 | 24396.87
Reading the curve
High T
Broad exploration, frequent uphill moves accepted
Cooling
Acceptance of worse moves tapers off
Low T
Search converges near the optimum and stabilizes
ASDR · Simulated Annealing Optimization
11

## Slide 12
Scope
Current assumptions & what's next
Simplifications made today
ΔV estimated from altitude & inclination differences
Simplified mission time model
Single-spacecraft mission
One weighted objective function
Static debris positions
No atmospheric drag or perturbations
Future improvements
Real orbital elements (Keplerian / TLE)
Hohmann & Lambert transfer calculations
Integration with Orekit or Poliastro
Multi-spacecraft mission planning
Ant Colony Optimization & PSO
NSGA-II multi-objective optimization
Real ESA DISCOS / Space-Track catalogs
ASDR · Simulated Annealing Optimization
12

## Slide 13
From simplified model to mission-ready planner
A simplified transfer model + weighted objective + Simulated Annealing already demonstrates the OR workflow — ready to be extended with real astrodynamics libraries and multi-objective search.
Kirkpatrick, Gelatt & Vecchi (1983) · Talbi (2009) · NASA ODPO · ESA Space Debris Office
For educational, academic, and research purposes